## Slide 1: Flexible Slender Bodies Control Thesis Progress Review 1
Anatole VERHAEGEN
Supervisor : Prof. Rafał Żbikowski
MBDA coordinator : Mr Graham Wallis

## Slide 2
Background Literature
Thesis Objectives & Schedule
Actual Progress

## Slide 3: Background Literature
Control of Flexible Structures
Modelling & Order Reduction
Sensors & Actuators Technology
Sensors & Actuators Placement

## Slide 4: Background Literature Control of Flexible Structures
Active flutter suppression*:
  Implemented by NASA in 1992
  Uses 1 accelerometer and 1 control surface
  Increases the flutter dynamic pressure
Flutter on a Glider
*M. R. Waszak and S. Srinathkumar, "Design and experimental validation of a flutter suppression controller for the active flexible wing", NASA Langley Research Center; Hampton, VA, United States Aug 1992

## Slide 5: Background Literature Control of Flexible Structures
Active flutter suppression
Large Space Structures attitude control*:
  Control of rigid-body modes and elastic modes
  Investigation of sensor and actuator placement
  Dissipative controllers advantages
*Joshi, S. M., Maghami, P. G. and Kelkar, A. G, “Dynamic dissipative compensator design for large space structures”, NASA Langley Research Center, 1991

## Slide 6: Background Literature Control of Flexible Structures
Active flutter suppression
Large Space Structures attitude control
Control of flexible structure during time-dependent maneuvres*:
  Association between flight dynamics and elastic modes
  Discrete-time approach
  Time-varying controller
*Meirovitch & Tuzcu, “Control of Flexible Aircraft Executing Time-Dependant Maneuvres”, AIAA 2004-1634, 2004

## Slide 7: Background Literature Modelling & Order Reduction
Accuracy of modelling:
*Jer-Nan Juang, “Applied System Identification, Prentice Hall“, 1994
Method | Accuracy on modes
Finite Element Method | 10%
1st Model Identification | 5%
2nd Model Identification | 1-2%
Error due to modelling methods*

## Slide 8: Background Literature Modelling & Order Reduction
Accuracy of modelling
Order reduction*:
  Truncation techniques ()
  Frequency weighted techniques
* Wodek K. Gawronski, “Dynamics and Control of Structures: A Modal Approach” (Mechanical Engineering Series) Hardcover – September 11, 1998
F-16 FEM : 166,536 nodes

## Slide 9: Background Literature Sensors & Actuators Technology
*S. Laflamme et al., “Soft Elastomeric Capacitor Network for Strain Sensing Over Large Surface”, IEEE 2013
Sensors:
  Accelerometers and gyrometers
  Strain gages
  Distributed sensor network*
6 Axis IMU
Strain Gages
Strain Sensor Network

## Slide 10: Background Literature Sensors & Actuators Technology
*G. Selince, “Un Nouveau Concept de Pilotage des Missiles Application Aux Sol-Air“ - AEROSPATIALE - DIVISION DES ENGINS TACTIQUES
Ϯ V. Viti, R. Neel, and J. A. Schetz, “Detailed flow physics of the supersonic jet interaction flow field” - PHYSICS OF FLUIDS 21, 046101 2009
Actuators:
  Ailerons
  Hot gas jets (PIF-PAF)*
  Cold gas jetsϮ
Lateral Jet Control*

## Slide 11: Background Literature Sensors & Actuators Placement*
Possible sensor location
Possible actuator location
* Wodek K. Gawronski, “Dynamics and Control of Structures: A Modal Approach” (Mechanical Engineering Series) Hardcover – September 11, 1998

## Slide 12: Thesis Objectives & Schedule
Objectives of the Thesis
Gantt Chart Schedule

## Slide 13: Objectives
Model an existing missile – Rigid-body modes + elastic modes
Make appropriate modifications (actuators / sensors)
  Cost-effective
  Not intrusive
Design an implementable controller
  Double the bandwidth of the system
  Same performance with a lighter structure
  Halve vibrations magnitude

## Slide 14: Gantt chart
2015
2015
Today
February
March
April
May
June
July
August
Choice of Missile & Modifications
18/5/2015
Final Model Complete
16/6/2015
Final Controller Designed
12/7/2015
Thesis Progress Review 2
13/7/2015
Thesis Hand-in
12/8/2015
Literature Review
Lumped Element Model Studies
FEM & Aerodynamics Modelling
Specifications Definition
Controller Design
Performance Assessement
Thesis Writting

## Slide 15: Actual Progress
Lumped Element Models & Simulations
Contacts within MBDA

## Slide 16: Lumped Element Models Modelling
α1
α2
L2
L1
Turbulence
Thrust vector control
Structural model :
2 rigid rods
1 torsion spring (1% damping)
Constant mass
Aerodynamic model :
Lift applied at CG of each rod
Mach 4.5
Von Karman turbulence model
ASTER 30 - Anti-Ballistic Missile
(Surface-To-Air)
Details

## Slide 17: Lumped Element Models Simulation
Controller designed without elastic modes
Controller designed with elastic modes

## Slide 18: Contacts within MBDA
MBDA Coordinator: Mr Graham Wallis – 08/04, 24/04. Next : 18/05
Visit of BAe ATC – End of May
Meeting with an MBDA control engineer – 18/05

## Slide 19: Thank you

## Slide 20
2015
2015
Today
February
March
April
May
June
July
August
Choice of Missile & Modifications
18/5/2015
Final Model Complete
16/6/2015
Final Controller Designed
12/7/2015
Thesis Progress Review 2
13/7/2015
Thesis Hand-in
12/8/2015
Literature Review
Lumped Element Model Studies
FEM & Aerodynamics Modelling
Specifications Definition
Controller Design
Performance Assessement
Thesis Writting